## Slide 1: Chesapeake Bay Program Incorporation of Lag Times into the Decision Process
Gary Shenk
10/16/12

## Slide 2: Chesapeake Bay Program Does Not Incorporate Lag Times into the Decision Process

## Slide 3: No Lag in Model or TMDL
The goal of the TMDL and the Watershed Implementation Plans is to have practices in place by 2025 that will eventually lead to meeting the water quality standards
Watershed model scenario mode:
  The long-term annual average loads given land use, land management, BMPs, point sources, atmospheric deposition, etc at steady state.

## Slide 4: Chesapeake Bay Partnership Models

## Slide 5
Annual, monthly, or
daily values of
anthropogenic factors:
Land Use Acreage
BMPs
Fertilizer
Manure
Tillage
Crop types
Atmospheric deposition
Waste water treatment
Septic loads
Hourly or daily
values of
Meteorological
factors:
Precipitation
Temperature
Evapotranspiration
Wind
Solar Radiation
Dew point
Cloud Cover
Daily flow, nitrogen,
phosphorus, and
sediment compared
to observations
over 21 years
How the Watershed Model Works
HSPF
Calibration Mode

## Slide 6: Each segment consists of 30 separately-modeled land uses:
6
Regulated Pervious Urban
Regulated Impervious Urban
Unregulated Pervious Urban
Unregulated Impervious Urban
Construction
Extractive
Combined Sewer System
Wooded / Open
Disturbed Forest
Corn/Soy/Wheat rotation (high till)
Corn/Soy/Wheat rotation (low till)
Other Row Crops
Alfalfa
Nursery
Pasture
Degraded Riparian Pasture
Afo / Cafo
Fertilized Hay
Unfertilized Hay
  Nutrient management versions of the above
Plus: Point Source and
Septic Loads, and
Atmospheric
Deposition Loads
Each calibrated to nutrient and
Sediment targets
How the Watershed Model Works

## Slide 7: Two Separate Segmentation Schemes
A land use within a land segment has the same inputs
  atmospheric deposition
  fertilizer
  manure
  precipitation
Land segmentation driven by availability of land use data
Land segments determined by
  County lines
  Rainfall Variances
  Federal / Non-Federal

## Slide 8: Land Simulation – 1 Acre 4 completely mixed soil layers
Ground Water
Surface
Interflow
Lower Zone

## Slide 9
Trees
Roots
Leaves
Particulate
Refractory
Organic N
Particulate
Labile
Organic N
Solution
Ammonia
Nitrate
Solution
Labile
Organic N
Adsorbed
Ammonia
Solution
Refractory
Organic N
Storages can Build up in the landscape
Atmospheric Deposition
Denitrification
Export
Export
Export
Export
Export
Export
Export

## Slide 10
Precipitation
Fertilizer
Manure
Atmospheric deposition
Runoff
How the Watershed Model Works
Hydrology
submodel
Management filter
River
Sediment
submodel
Phosphorus
submodel
Nitrogen
submodel
}
hourly

## Slide 11: Scale in Phase 5 - Sediment
BMP Factor
Land Acre Factor
Delivery Factor
Edge of Field
Expected loads from one acre
Edge of Stream
60-100 sq miles
In Stream Concentrations
Scour/
Deposition
Notes: For any particular watershed, the single simulated acre is multiplied by the number of acres of that land use in the watershed.
The different types of land uses are added together to get the total load to the stream.
The stream then has some scour and deposition depending on the velocity of the water

## Slide 12
Phase 5 river segmentation
A river segment gathers inputs from the watershed and has one simulated river
Consistent criteria over entire model domain
  Greater than 100 cfs
    or
  Has a flow gage

## Slide 13
Constant values of
anthropogenic factors:
Land Use Acreage
BMPs
Fertilizer
Manure
Tillage
Crop types
Atmospheric deposition
Waste water treatment
Septic loads
Hourly or daily
values of
Meteorological
factors:
Precipitation
Temperature
Evapotranspiration
Wind
Solar Radiation
Dew point
Cloud Cover
Run for 1984-2000
Average 1991-2000
For ‘flow-normalized average annual loads’
How the Watershed Model Works
HSPF
Scenario Mode

## Slide 14: Nitrogen Loads Delivered to the Chesapeake Bay By Jurisdiction Point source loads reflect measured discharges while nonpoint source loads are based on an average-hydrology year
14
333.9
289.9
281.1
270.2
175
266.3
277.7
275.1
262.9
261.9
260.7
184.4
183.1
Phase 4.3 Data

## Slide 15: Lag Time
Calibration – the WSM is calibrated to observed data, so including important lagged processes would improve calibration
Validation of predictions – if the WSM is predicting changes in nutrient loads that are not seen in the monitoring data, would lags help to explain the difference.
Communication – When will the Chesapeake Bay respond to management actions