## Slide 1: Drying and wetting cycles of normally wet soils impact soil respiration and health
François Birgand1, Augustin Thomas6, Bryan Maxwell1, Louis Schipper4, Laura Christianson2, Matt Helmers3, Mohamed Youssef1, Shiying Tian1, David Williams5, George Chescheir1, Wenlong Liu1
1
3
4
2
5
NIFA Award #: 2016-67019-25279 Multistate S1063
6

## Slide 2
What are woodchip bioreactors?
Agricultural BMP
Intercept tile drainage
Targets nitrate removal
~20 year lifespan
NRCS approved
2-22 g N m-3 d-1 in field
Mainly seen in Midwest
Christianson and Helmers, 2011

## Slide 3: From the literature
Reported nitrate removal efficiencies varying from less than 10% to more than 90%
Decrease of removal efficiency within 1 to 5 years from >60% to <20%

## Slide 4: Research questions
Can we find a practical way to increase denitrification in woodchip bioreactors?
What are the impacts of Draining ReWetting cycles on respirations to normally saturated soils?
Can we identify the microbial pathways in bioreactors?
Are microbiologically driven reactions slow or rapid in soils?
Are we learning something new from high resolution aqueous and gaseous concentration data?
Could we use simplistic soil models to learn the role of DOC quantity and quality to soil health?

## Slide 5: Hypotheses
Drying and ReWetting (DRW) cycles can ’rejuvenate’ woodchip bioreactor
Gaseous emission data will provide information on the microbial pathways during DRW

## Slide 6
Black Box

## Slide 7: Objectives
Track and quantify the fate of water, nitrate, and DOC to reconstruct the apparent functioning
Measure in the lab and in the field the aqueous and gaseous removals and emissions associated with the use of bioreactors
Find solutions to ’rejuvenate’ woodchip bioreactor
Identify the microbial pathways using isotopic signatures
Integrate this new knowledge into 2D biogeochemical computer models
Use the models to explore and define novel and optimized design and management guidelines

## Slide 8: Method
Use high resolution instruments to measure gaseous and aqueous concentrations
Lab column experiments
2-5 week long experiments in field bioreactors in North Carolina, Iowa, New Zealand
Process-based modeling

## Slide 9
What are drying-rewetting cycles?
Cycle between dry/wet conditions
Gradient of conditions
Based on literature:
  Stimulates respiration
  Increases mineralization of C & N
  Changes in microbial community
Dry
Unsaturated
Wet
Saturated

## Slide 10
Experimental Hypothesis
Do drying-rewetting cycles in woodchip bioreactors significantly improve treatment performance by increasing nitrate removal rates?
denitrification…
Aerobic breakdown
increases available carbon
+ Carbon
DENITRIFICATION!!!

## Slide 11
Materials and methods
DRW 2017
297 days
Experiment #1
DRW
SAT
Eight woodchip-filled columns
Continuous upflow (~8 hr HRT) for 297 days.
Two treatment groups (n=4)
  SAT – Constant saturation
  8 h DRW – Drained once a week, unsaturated for 8 hours.
Outlet [NO3] measured every 2 h using small-volume MPS

## Slide 12
Materials and methods
DRW 2018
105 days
Experiment #2
Same columns used in previous experiment.
Continuous upflow (~8 hr HRT) for 105 days.
Four treatment groups (n=2)
  SAT – Constant saturation
  2 h DRW – Unsaturated for 2 h
  8 h DRW – Unsaturated for 8 h
  24 h DRW – Unsaturated for 24 h
Experiment #1
DRW 2017
297 days
2 h DRW
SAT
8 h DRW
24 h DRW
Outlet [NO3] measured every 2 h using small-volume MPS

## Slide 13
Upflow columns
INFLOW: peristaltic pump
OUTFLOW
50 cm of 6-year-old woodchips
Washed gravel underbed
Nylon mesh separating gravel and woodchips
36 cm head space

## Slide 14
Multiplexed high frequency measurements
INFLOW rates: bidaily
OUTFLOW WQ
Lab microvolume MPS
Maxwell et al.,
HESS, 2018
NO3- + DOC: 2-hourly
CO2
N2O + isotopes: 1 Hz -> hourly
QCL
Aqueous
Gaseous
QCL

## Slide 15
Materials and methods: Lab column set-up

## Slide 16: Water quality results

## Slide 17
Results, DRW 2017 : High frequency data
84 measurements per column per week
8 h DRW

## Slide 18
Results, DRW 2017 : High frequency data
640 measurements per week for all columns
8 h DRW

## Slide 19
Results, DRW 2017 : High frequency data
Weekly DRW cycle
8 h DRW

## Slide 20: Volumetric Removal and Production rates
RNO3 = mass removed / volume of bioreactor / time
PDOC = mass added / volume of bioreactor / time

## Slide 21
Results, DRW 2017 : Nitrate removal rates, RNO3
Significant differences in RNO3 between groups after the 2nd DRW cycle.

## Slide 22: Rapid and Large response to DRW cycles
RNO3
PDOC

## Slide 23: Slow or rapid reactions in soils?
Suggestion:
There is a potentially very rapid component of microbially mediated processes in soils

## Slide 24
Results, DRW 2018 : Volumetric NO3 removal rates
Weekly DRW period

## Slide 25
Results, DRW 2018 : Volumetric NO3 removal rates

## Slide 26: DRW cycles increase nitrate removal
90% to 172% increase for 24 hr DRW cycle; 8 h DRW increased by 35 – 70%
Increase in RNO3 by ~5 percentage points for every hour woodchips were unsaturated

## Slide 27: What causes the increased nitrate removal?

## Slide 28
Increased DOC production fuels increased NO3- removal

## Slide 29
Predicted RNO3 (g N/m3/d)
Measured RNO3 (g N/m3/d)
Measured RNO3 (g N/m3/d)
Measured RNO3 (g N/m3/d)
T°C effect
T°C effect + PDOCnet
T°C effect + PDOCnet +
Negative HRT
=

## Slide 30: Water quality take home points
Yes! DRW have the potential to ’rejuvenate’ nitrate removal efficiency, at least in the lab
DRW cycles seem to generate higher quantity (and quality?) of labile carbon, which fuel nitrate removal

## Slide 31: Gaseous emission results

## Slide 32: A system opened to the atmosphere

## Slide 33: Bulk CO₂ values, a clear typology
Notes: Shoe typology for CO2, not so for N2O

## Slide 34: Long DRW cycles diminish N₂O emissions

## Slide 35: Small percentage of N lost as N₂O emissions
In the water, removal rate of:
In the air, emission of:
0.2 % of denitrified N is emitted as N₂O
BUT, we expect most of the N₂O to remain dissolved over the length of the experiment

## Slide 36: Bulk CO₂ values, a clear typology
Notes: Shoe typology for CO2, not so for N2O

## Slide 37: An evolution in emission pathway over the weeks

## Slide 38: Concluding remarks
DRW cycles have the potential to largely increase nitrate removal rates in woodchip bioreactors
Linear increase in removal rates as a function of DRW duration
Aerobic-based processes stimulate higher quantity (+ quality?) of DOC which fuels denitrification
  Rapid response (hours) : due to the rapid actuation of extracellular enzymes in soils?
  Slower response (weeks): adaptation by microbes/fungi to predictable DRW cycles?
  What if the DRW cycles are not predictable?
  Several stage microbial adaptation process?

## Slide 39: Concluding remarks
Are we learning something new from high resolution aqueous and gaseous concentration data?
  Gives unprecedented chances to improve our models
  Gives opportunities to see new things

## Slide 40: High spatio-temporal resolution data in the field
Plymouth, NC
Nashua, IA
Tatanui, NZ

## Slide 42
Wells at 0.5 m from inlet

## Slide 43
Wells at 3.2 m from inlet

## Slide 44
Wells at 5.9 m from inlet

## Slide 45
Wells at 8.5 m from inlet

## Slide 46: Concluding remarks
Could we use simplistic soil models to learn the role of DOC quantity and quality to soil health?
  I think so!
  Using woodchip bioreactors as a simplistic model is very attractive:
    Homogeneous source of carbon (simpler microbiome?)
    Large redox gradients from aerobic to anaerobic conditions
    Can be used in the lab and in the field
    Access to water to measure all sorts of indicators at a high resolution

## Slide 47
Acknowledgements
Funding Source
Facilities and Lab Analysis
Microbial Analysis