## Slide 1: Drainage Water Management: For what purpose? Linking Soil and Watershed Health to In-field and Edge-of-Field Water Management
Dr. Ray B. Bryant, Research Soil Scientist USDA-ARS Pasture Systems and Watershed Management Research Unit University Park, PA
2020 STAC Workshop

## Slide 2: How does tile drainage affect soil health?
Increases aeration of the rooting zone
  Allows growth of beneficial crops that are not wetland tolerant
Increases rate of oxidation of organic matter in the surface horizon
Decreases reduction of nitrate, manganese and iron
  Nitrate remains available for leaching to tile drains
  Iron that stays in oxide form sorbs phosphorus
Decreases water storage capacity at field and landscape scale
Increases rate of water release (reduced residence time)
  Increases potential for downstream flooding

## Slide 3
Drainage Water Management
NRCS CP 554
30% TN, 0% TP, 0% Sed.

## Slide 4
NRCS Conservation Solutions…
Drainage Water Management
Adjustable Riser Boards
Raised Water Table
Saturated Soil
Water Level Control Structure
Dam
Reservoir
Sponge
“park your drain”
Healthy Soil, Bigger sponge

## Slide 5: How does drainage water management reverse adverse effects of drainage?
Decreases aeration of the rooting zone
  Will have negative effects on cover crops that are not water tolerant
Decreases rate of oxidation of organic matter in the surface horizon
Increases reduction of nitrate, manganese and iron
  Nitrate undergoes denitrification to atmospheric nitrogen
  Iron oxides may reduce and release phosphorus into solution
Increases water storage capacity at field and landscape scale
Decreases rate of water release (increased residence time)
  Decreases potential for downstream flooding unless heavy rain falls on a saturated soil

## Slide 6
Conservation Practice Standard Code 333:
Amending Soil Properties with Gypsiferous Products

## Slide 7: Purpose: Improve soil physical/chemical properties to increase infiltration and reduce soil erosion
Additional Criteria:
Apply 1.5 tons/acre of gypsum.
Agricultural Research Service
Treated w/ FGD
Not Treated
Treated
Not Treated
Ponding/Redox
Photo courtesy of Darrell Norton

## Slide 9
6/1

## Slide 10
INTRODUCTION
CONCLUSIONS

## Slide 11
SUMMER 2018
SUMMER 2019
NDVI

## Slide 12
Prevented Planting Areas
Hutchinson County, SD
Lincoln County, MS

## Slide 14
Prevented Planting Areas
Hutchinson County, SD
Lincoln County, MS

## Slide 15
NRCS Conservation Solutions…
Drainage Water Management
Adjustable Riser Boards
Raised Water Table
Saturated Soil
Water Level Control Structure
Dam
Reservoir
Sponge
Healthy Soil, Bigger sponge
“Dynamic drainage water management”

## Slide 16: Closing Questions
Can drainage water be managed “dynamically” to reduce risks of downstream flooding?
Is downstream flooding a problem in the Chesapeake Bay Watershed?
What are the effects of “parking your drain” on cover crops?
What are the effects of “dynamic” drainage water management on cover crops?
Do we need different cover crops for use under “park your drain” management?
What is the fate of phosphorus under drainage water management?