## Slide 1: Connecting Soil Health and Watershed Health
Mark Tomer
USDA-Agricultural Research Service
Ames, Iowa

## Slide 3
Pre-settlement soil surface
Post-settlement
alluvium

## Slide 4
Disclaimer:

## Slide 5: Deep Loess Research Station: Watersheds & Experimental design
Conventional Tillage:
1971-1995
Ridge Tillage:
1971-1995
(plus terraces)

## Slide 6
The conservation watershed showed lower bulk density (by 0.08 Mg m-3), and higher organic carbon content (by 0.42% mass).
Implications for field water contents?

## Slide 7: Effect of conservation practices on stream hydrology: flow duration curves
baseflow
Conventional-till
Ridge-till
runoff
Conventional-till
Ridge-till

## Slide 8
After each of four droughts, baseflow recovered more rapidly in watersheds under conservation tillage than those under conventional tillage

## Slide 9
Impact of management change:
Conventionally tilled watersheds both converted to no-tillage in 1996,
With a Corn-soybean rotation in W1, and a
Six-year (CSCAAA) rotation in W2

## Slide 10: Changes in NO3-N and total P concentrations during a runoff event

## Slide 11: Nutrient Transport: General Truths Contrasting N versus P
Nitrogen:
Biologically complex
Dominant form is a gas
Easily leached from well-drained soils
Subsurface transport
Seasonally dynamic
Released from saturated soils as a gas
Phosphorus:
Chemically complex
Not any gaseous form
Strongly adsorbed in well-drained soils
Surface transport
Episodically dynamic
Released from saturated soils in dissolved form

## Slide 12
No-tillage
Conservation crop rotation

## Slide 13
Agricultural Conservation Planning Framework:
A data-driven toolset for watershed conservation and landscape research

## Slide 14
Define Watersheds to each stream segment
Split watersheds by stream
ACPF Version 3 - Riparian catchments: Discretizing watersheds by riparian segment lengths

## Slide 15
Research results on landscape capacities-
Quantifying water storage capacities of different landscapes based on specific practices (flood water detention)
Quantifying densities at which different EOF practices can be placed (siting potentials)
Quantifying saturated buffer placements relative to distribution of tile drainage
Prioritizing locations where riparian buffers can treat disproportionate delivery of nutrients from cropland

## Slide 17: Summary
Soil improvement has significant potential to reduce impacts of flood and drought.
Diversified crop rotations provide important options for soil improvement and addressing environmental trade-offs often associated with conservation management.
Analysis tools are available that enable researchers to develop a greater landscape-based cognizance of opportunities and challenges for soil and water conservation unique to any given watershed.

## Slide 18: QUESTIONS?