## Slide 1: The Chesapeake Bay Program Watershed Model Processes and Results
Gary Shenk – CBPO
Based on the work of:
Lewis Linker, Gopal Bhatt, Isabella Bertani, Jeff Sweeney, Jessica Rigelman, Olivia Devereux, Matt Johnston, Andrew Sommerlot, Richard Tian, Danny Kaufman, Ruth Cassilly and many, many more
Presentation to STAC
12/18/2019
This information is being provided to meet the need for timely best science. The information is provided on the condition that neither the U.S. Geological Survey nor the U.S. Government shall be held liable for any damages resulting from the authorized or unauthorized use of the information.

## Slide 3: Time-Averaged Model
Direct Loads
Average Load + Inputs * Sensitivity
Land Use Acres
BMPs
Land to Water
Stream Delivery
River Delivery
*
*
*
*
*
Keep It Simple
Include Everything
Load per land use per area

## Slide 4: Time-Averaged Model
Time averaged scenario output
Estimates the long-term average load given a set of anthropogenic inputs
Connected to a dynamic model for calibration and to estimate some sensitivities
Direct Loads
Average Load + Inputs * Sensitivity
Land Use Acres
BMPs
Land to Water
Stream Delivery
River Delivery
*
*
*
*
*
CAST
Load per land use per area

## Slide 5
Include Everyone

## Slide 7
LOCAL POPULATION PROJECTIONS
CBLCM v4
2010 - 2050
Modeling Assumption:
Urban development results from growth in population and employment.
Modeling the Effects of Population Growth on Land Use Change and Pollutant Loads

## Slide 8
  Chesapeake Bay Land Change Model v4
County-level Population Projections
County-level
Employment Projections
Commercial Development
Residential Development
Housing Density
Road Gravity
Residential Probability
Unprotected and Developable
Job Density
Road Gravity
Commercial Probability
Unprotected and Developable
Potential
Infill
Development
Total Housing
Demand
Housing Land Demand
Employment Land Demand
Future Land Cover
Present
Land Cover
Future Development Statistics
Summary Units
(P6 modeling segments)
Historic
Development
Patterns
Historic
Infill
Patterns
Iterative & Stochastic
Land Conservation
Road Gravity
Conservation Probability
Unprotected
Land Conservation Demand
Notes: Accessibility = peak travel times for single-occupancy vehicles between transportation modeling zones.

## Slide 9
Multiple Stochastic Iterations
Every county is simulated 101 times for each scenario and target year, i.e., 2025.
Average of simulations by summary unit = future development
Relative Standard Deviation = estimate of uncertainty

## Slide 10: Point Sources
Most WWTP use default values for load based on flow and technology
  about 10% use monitored values
  Makes up about 85% of the load
Industrial sources are monitored
States estimate industrial sources to increase based on population trend, linear trend, or no trend

## Slide 11
Sewer Service Area
Residential Growth (sim.)
Commercial Growth (sim.)
Forecasted 2025 Growth on Sewer vs Septic in Maryland

## Slide 12: Atmospheric Deposition Model
Regression model for history of wet deposition
Hourly estimate based on
  Weather
  Physical landscape
  Upwind sources

## Slide 13: Atmospheric Deposition Model
CMAQ National-scale EPA model
Used for many national air regulations
CBP uses dry deposition and changes in future wet and dry deposition due to policy

## Slide 14: Fine-scale spatial analysis to improve sediment prediction

## Slide 15: Sources
WQGIT determines inputs
  Ag Workgroup
    Ag Modeling Subcommittee
    Poultry Litter Subcommittee
    Riparian Pasture Deposition Subcommittee
    …
  Urban workgroup
  Wastewater Treatment Workgroup

## Slide 18: Soil P data – Lancaster
Soil Test Data
Mass-Balance Process Model
Bayesian Estimate

## Slide 19: Nitrogen in Groundwater
Used MODFLOW models of Potomac and Eastern Shore from Ward Sanford
Coastal Plain – PC regression model
Others – related to recharge and depth to groundwater

## Slide 20: Flowpath Lags
Used in dynamic model for calibration
Not used in scenarios

## Slide 21: Management Practices – BMP Panel Results
CBP partnership asks for a panel (WQGIT)
Panel forms for 1-2 years
  At least six subject matter experts
  Academics
  Implementers
  Government scientists
  …
After approval by the partnership, it is included in the watershed model

## Slide 22: BMPs
189 BMPs with specified percent reduction
104 are cover crops
  Cover Crop Traditional Rye Early Drilled
  Cover Crop Traditional Forage Radish Early Aerial
    Appalachian Plateau Siliciclastic TN 11% TP 6% TSS 9%
    Coastal Plain Dissected Uplands TN 14% TP 6% TSS 9%

## Slide 24
Feed Additives
Stream Fencing
Lagoon Covers
Manure Storage
Manure transport
Nutrient
management

## Slide 25
Land to Water factors
Nitrogen
Groundwater recharge
Piedmont Carbonate
Enhanced Vegetative Index
Available water capacity
USGS
Sparrow Model

## Slide 26
Stream to River factors
Nitrogen
Temperature
Travel time
Reservoirs

## Slide 27
Stream to River factors effect
Project/Decision
Endpoint
Data Set
Model
BMP effectiveness change
Land to water factor effect
Groundwater Travel Time effect
WWTP and septic
Effect
Diversion
Effect
CMAQ
Climate change effect
Soil P history
effect
RCP
Process-based response of flow and sediment
On land
Specified land nutrient response
Estuarine Model
WQSTM
Effect on water quality standards
Climate scenarios
Management Effort Adjustment
Streams
Effect on land use
Effect on Ag
Rivers
Support/Revise
Flow--N relationship
Investigate
Speciation changes
P sensitivity in developed
Wetlands losses and gains
Sea level Rise
Reasonable response to sea level rise?
STAC CC2.0
Framework recommendations
Observed Precipitation Trends
BMPs
Land to Water
Growth and respiration curve for phytoplankton
Wind effects
Ocean Temp
UNEC
CSO
Effect
Nutrient Inputs
GCMs
Extrapolation
Included
Not included
But important
Down-scaling
GCM
Selection
Estuarine Inputs
Reasonable response to temperature?
Not included
minor
Climate
Watershed
Estuary
Management
Carbon Dioxide effect
Loads from flooding
Reservoir Rules effects

## Slide 29
How well does the model predict spatial differences in load?
WRTDS Per Acre Load
Simulated Per Acre Load

## Slide 30
How well does the model predict Temporal differences in load?
CBP loads indicator and CAST scenarios

## Slide 33: 34 stations with long-term data
1985-2014
WRTDS trends
CAST scenarios with constant atmospheric deposition
WRTDS more variable
Average reduction similar
74% directionally correct
Nitrogen

## Slide 34: 15 stations with long-term data
1985-2014
WRTDS trends
CAST scenarios
WRTDS more variable
Average reduction similar when there are reductions
73% directionally correct
Phosphorus

## Slide 35: 319 5-year trends
1985-2014
WRTDS trends
CAST scenarios with constant atmospheric deposition
WRTDS more variable
58% directionally correct
Likely too short of a time frame
Nitrogen

## Slide 36: 180 5-year trends
1985-2014
WRTDS trends
CAST scenarios
WRTDS more variable
Average reduction similar
59% directionally correct
Phosphorus

## Slide 37
Nitrogen

## Slide 38
Phosphorus

## Slide 39
Nitrogen

## Slide 40
Phosphorus

## Slide 41: Further investigation
Include atmospheric deposition
What is the effect of lag times
Investigate uncertainty of both WRTDS and CAST
Attempt to isolate factors =>