## Slide 1: CAST Optimization: Intermediate Status Kalyanmoy Deb, Pouyan Nejadhashemi, Gregorio Toscano, and Hoda Razavi
Michigan State University
Meeting with STAC Members
June 13, 2023

## Slide 2
Agenda
Introduction to Michigan State University (MSU) Team
1
STAC Workshop Report, 2016: Goals and Applications
2
Objectives and Main Tasks of the Project
3
Current Status of the Project
4
Short Demo (video)
5
Future Plan
6

## Slide 3: Kalyanmoy Deb
Title:
  University Distinguished Professor
  Koenig Endowed Chair Professor
    Dept of Electrical and Computer Engineering
    Dept of Computer Science and Engineering
    Dept of Mechanical Engineering
Expertise and Achievements:
  Optimization, Multi-objective optimization, Machine Learning, Modeling
  36 years of experience in optimization and its applications
  Author of popular evolutionary optimization methods: NSGA-II, NSGA-III
  Author of two text-books on optimization, 610 research papers
  185,000 Google Scholar citations, h-index: 133
  Director, Computational Opt. and Innovation (COIN) Lab at MSU

## Slide 4: Pouyan Nejadhashemi
Title:
  University Foundation Professor
    Department of Biosystems and Agricultural Engineering
    Department of Plant, Soil and Microbial Sciences
  Elected board member
    International Environmental Modelling & Software Society
Expertise and Achievements:
  Soft computing applications in water resources management
  Computational Ecohydrology
  Evaluation and development of watershed and water quality models
  $41M in grant funding
  130 peer-reviewed publications
  180 scientific presentations
  Director, Center for Intelligent Water Resources Engineering (CIWRE)

## Slide 5: Gregorio Toscano
Title:
  CBPO CAST optimization researcher
  Associate Professor - Center for Research and Advanced Studies, Mexico
  PhD in Evol. Multi-Criterion Optimization, 2005
Expertise and Achievements:
  Multi-objective optimization, Computational Intelligence, and Machine Learning
  Multi-objective Micro-GA, Multi-objective PSO
  Full Stack
  Programming Languages
  7,692 Google Scholar citations

## Slide 6: Hoda Razavi
Title:
  PhD Student, Biosystems and Agricultural Engineering, Michigan State University
  MS Water and Hydraulic Structures, Civil Engineering, Khajeh Nasir Toosi University of Technology
  BS Civil Engineering University of Tehran
Expertise:
  Watershed/water quality modeling
  Environmental flow
  Multi-objective optimization
  Uncertainty quantification
  Water resources management
  Data-driven models
  Climate change impacts

## Slide 7
Goals:
Cost minimization was a key goal for the partners
Maximizing co-benefits, particularly those supporting Chesapeake Bay Watershed Agreement goals
Maximizing load reduction reliability
Equitable distribution of effort among jurisdictions
Equitable distribution of effort among source sectors
Limits on retirement of agricultural land
Ability to use the tool at various scales
“Cracking the WIP” - Designing an Optimization Engine to Guide Efficient Bay Implementation STAC Workshop Report, 2016

## Slide 8: Applications: STAC Workshop Report, 2016
Under development | Future Application | 
Address optimization of multiple co-benefits Minimize costs of BMP implementation Optimal use of BMPs on land use by county Make Bay TMDL load targets achievable Make Phase III WIP scenario that achieves nitrogen, phosphorus, and sediment targets for the lowest cost with the ability to tweak to see the different scenario costs | Rethink the allocation of responsibilities by sector, by geography, by funding Recognize the value/influence of ecosystem services in local decision making Assist with the development of grant applications Help local governments document co-benefits of WIP implementation Identify cost savings within a source sector | Provide a basic resource for planners to understand advantages and disadvantages of implementation options Assist progress towards other management strategy objectives Help in development of state implementation plans (Bay Milestones and WIPs) Help in development of local implementation plans (local and Bay TMDLs) Develop sector implementation plans cost effectively

## Slide 9: Objective of the MSU-Optimization Project
Investigate, develop, program, verify, and implement an optimization system built around the CBP’s CAST Model to:
Improve the water quality
At the lowest cost

## Slide 10: Timeline of the Project
Show our plan here
We are here
Notes: Pouyan asked to change the tasks names.
GT: Tasks names updated.

## Slide 11: Timeline of the Project
Show our plan here
We are here
Notes: Pouyan asked to change the tasks names.
GT: Tasks names updated.

## Slide 12: Timeline of the Project
Show our plan here
We are here
Notes: Pouyan asked to change the tasks names.
GT: Tasks names updated.

## Slide 13: Timeline of the Project
Show our plan here
We are here
Notes: Pouyan asked to change the tasks names.
GT: Tasks names updated.

## Slide 14: Timeline of the Project
Show our plan here
We are here
Notes: Pouyan asked to change the tasks names.
GT: Tasks names updated.

## Slide 15: Related Optimization Research at MSU
A case study on a billion-variable resource allocation problem
Point and population-based optimization and their combined use
  Evolutionary multi-objective optimization (EMO) algorithms to find multiple Pareto solutions
  "Innovization": Knowledge extraction from learning from Pareto solutions
  Multi-criterion decision-making (MCDM) to choose a preferred Pareto solution
Multi-objective optimization (MO) and decision-making

## Slide 16: Point and Population Based Optimization Methods: Adv and Disadv
Linear
Programming
Nonlinear Programming
Math. optimization
Evolutionary optimization
Point-Based
Population-Based
Other Metaheuristics
Search for a point which minimizes an
objective function satisfying constraints
Single-obj Opt.:
Best for
simplistic problems, difficult to modify for different problem classes
Ideal for local search
Best for
complex problems, flexible to suit a problem class
Ideal for global search

## Slide 17
Casting scheduling problem requiring 50,000 variables
CPLEX software could not solve 2,000-variable version
Customized Evol. Algorithm (population based) solves Billion-variable version
  Polynomial time performance
Population-based Optimization: A Case Study on Resource Allocation Problem
Deb, K. and Myburgh, C. (2017). A Population-Based Fast Algorithm for a Billion-Dimensional Resource
Allocation Problem with Integer Variables. European Journal of Operational Research, 261(2), 460–474.

## Slide 19: Chesapeake Bay Watershed Optimization Problem
Allocate a specific BMP to
  Land River Segment (LRS)
  Agency
  Load source
Minimize {Cost, Loadings}
Large number of variables will require large computational time
Surrogate model:
(N2)
s: LRS
h: Agency
u: Load source
b: BMP

## Slide 20: Converting Multiple Objectives Into One
Convert second objective into a constraint
Epsilon-Constraint method
  Vary to generate a set of trade-off solutions

## Slide 22: Surrogate Model Error
10,000 BMP scenarios are evaluated using surrogate model and CAST on West Virginia counties
Supports the use of surrogate model based optimization, if needed
Observed small error in Nitrogen loading value
Surrogate Model Percent Error Compared To CAST

## Slide 23: Multi-Objective Optimization
Results in a set of Pareto-optimal solutions
Step 1: Find multiple trade-off solutions
Step 2: Choose a preferred solution
Evol. Multi-objective optimization (EMO)
NSGA-III can handle 2-15 objectives with constraints

## Slide 24: Customized NSGA-III for CBW Problem
NSGA-III initialized with Eps-Constraint solutions
Repair operator to fix constraint violation
Optimize surrogate model
Berkeley County
Toscano, G., Hernandez-Suarez, J. S., Blank, J., Nejadhashemi, P., Deb, K. and Linker, L. (2022). Large-scale Multi-objective Optimization for Water Quality in Chesapeake Bay Watershed. Proceedings of 2022 Congress on Evolutionary Computation (CEC-2022), IEEE Press. (pp. 1–8). BEST PAPER AWARD
At least 3 injected solutions make NSGA-III efficient
Major finding:

## Slide 26: API-based Linking of CAST with NSGA-III
Allows multiple users with different programming environments to interact
Makes application modular
Automatic Programming Interface (API)

## Slide 27: NSGA-III Linked with CAST
NSGA-III calls CAST to evaluate using Restful APIs
Mixed Heterogeneity:
  50/50: 50% surrogate, 50% CAST
  95/5: 95% surrogate, 5% CAST
  1: All surrogates, evaluate final solutions by CAST
Time (min)
Hypervolume (HV)
95/5 is almost as good but requires less time
Major finding:

## Slide 28: Alternate Solutions Using Multi-objective Optimization
Evaluate alternate solutions before picking a single preferred solution
Analyze solutions for extracting knowledge for future use

## Slide 29: Multi-County Optimization
Observation:
This provides promise for extending the proposed optimization method to multi-state and to watershed level
Major finding:
  Some combinations of counties make the problem easier to solve compared to individual counties
    Ex: Group gets optimized faster than Hampshire county
Berkeley
Grant
Hampshire
Group
Counties and Group

## Slide 30: “Innovization”
Innovation through Optimization
Finding patterns in Pareto-optimal solutions for knowledge discovery using AI/ML methods
Optimality conditions must manifest as common patterns
Extract patterns and re-optimize
Deb, K. and Srinivasan, A. (2006). Innovization: Innovating design principles through optimization. Proceedings of the Genetic and Evolutionary Computation Conference (GECCO2006), New York: The Association of Computing Machinery (ACM), (pp. 1629–1636)
A Gear-box design with 28 variables
Not much change in 27 variables
Large change in one variable

## Slide 32: Knowledge Discovery Using Optimization
What are the benefits of optimization?
  Identify the best solutions for the problem in hand.
  Generating knowledge to solve future problems.

## Slide 33: Innovization Analysis
1
What is innovization?
Learning from optimization results and introducing new ideas, products, and services different from the existing ones.
2
What innovization can do to CBPO?
Provide information for better decision-making for BMP selections (farmers)
Identify the high priority areas for BMP implementation (regulators)
Help with resources allocation (policymakers)

## Slide 34: Methodology
BMP Selection ranking methodology based on Land use:
Overall goal: learn from optimization results to
Examine different ranking methodologies to identify the top BMPs,
1
Identify the similarities and differences between top-ranked BMPs,
2
Provide recommendations to reduce the optimization time
3

## Slide 35: Methodology
BMP Selection ranking methodology based on Land use:
In West Virginia, we identified the top two counties with the highest areas of urban and agricultural land uses.
(Berkeley and Mineral): Urban dominated
(Jefferson and Hardy): Agricultural dominated
Notes: Our study area is West Virginia. Based on the total land use area in West Virginia, we identified the top two countries with the highest areas of urban and agricultural land uses for innovization.
Study area: WV

## Slide 36: Methodology
1
Running CAST-optimization algorithm resulted in 220 solutions for each county
2
2420 solutions for 11 counties in about thousands land river segments.
3
Identified the best solutions from optimization.

## Slide 37: Methodology
Ranking methodology 1) rank the top BMPs based on the implementation acreages;
Ranking methodology 2) rank the top BMPs based on the percentage of maximum allowable acreages;
Ranking methodology 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.
Examine different ranking methodologies to identify the top BMPs,
1
1
2
3
Notes: Item 1) We propose three ranking strategies from the Pareto front:
Strategy 1) rank the top BMPs based on the implementation acreages;
Strategy 2) rank the top BMPs based on the percentage of maximum allowable acreages for specific BMPs;(every BMP does not apply to a certain place, this metric tells us what proportion of this allowable isused by our solutions.
Strategy 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.

## Slide 38: Methodology
Ranking methodology 1) rank the top BMPs based on the implementation acreages;
Ranking methodology 2) rank the top BMPs based on the percentage of maximum allowable acreages;
Ranking methodology 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.
Ranking methodology1):
BMP1
BMP2
BMP3
Examine different ranking methodologies to identify the top BMPs,
1
BMP1
BMP2
BMP 3
Notes: Item 1) We propose three ranking strategies from the Pareto front:
Strategy 1) rank the top BMPs based on the implementation acreages;
Strategy 2) rank the top BMPs based on the percentage of maximum allowable acreages for specific BMPs;(every BMP does not apply to a certain place, this metric tells us what proportion of this allowable isused by our solutions.
Strategy 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.

## Slide 39: Methodology
Ranking methodology 1) rank the top BMPs based on the implementation acreages;
Ranking methodology 2) rank the top BMPs based on the percentage of maximum allowable acreages;
Ranking methodology 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.
Ranking methodology 2):
BMP3
BMP2
BMP1
Examine different ranking methodologies to identify the top BMPs,
1
BMP1
BMP2
BMP 3
Notes: Item 1) We propose three ranking strategies from the Pareto front:
Strategy 1) rank the top BMPs based on the implementation acreages;
Strategy 2) rank the top BMPs based on the percentage of maximum allowable acreages for specific BMPs;(every BMP does not apply to a certain place, this metric tells us what proportion of this allowable isused by our solutions.
Strategy 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.

## Slide 40: Methodology
Ranking methodology 1) rank the top BMPs based on the implementation acreages;
Ranking methodology 2) rank the top BMPs based on the percentage of maximum allowable acreages;
Ranking methodology 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.
Ranking methodology3):
BMP2 ($12/lb N)
BMP3 ($15/lb N)
BMP1($24/lb N)
Examine different ranking methodologies to identify the top BMPs,
1
BMP1
BMP2
BMP 3
Notes: Item 1) We propose three ranking strategies from the Pareto front:
Strategy 1) rank the top BMPs based on the implementation acreages;
Strategy 2) rank the top BMPs based on the percentage of maximum allowable acreages for specific BMPs;(every BMP does not apply to a certain place, this metric tells us what proportion of this allowable isused by our solutions.
Strategy 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.

## Slide 41: Methodology
Ranking methodology 1) rank the top BMPs based on the implementation acreages;
Ranking methodology 2) rank the top BMPs based on the percentage of maximum allowable acreages;
Ranking methodology 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.
Ranking methodology1):
BMP1
BMP2
BMP3
Ranking methodology2):
BMP3
BMP2
BMP1
Ranking methodology3):
BMP2 ($12/lb N)
BMP3 ($15/lb N)
BMP1($24/lb N)
Examine different ranking methodologies to identify the top BMPs,
1
BMP1
BMP2
BMP 3
Notes: Item 1) We propose three ranking strategies from the Pareto front:
Strategy 1) rank the top BMPs based on the implementation acreages;
Strategy 2) rank the top BMPs based on the percentage of maximum allowable acreages for specific BMPs;(every BMP does not apply to a certain place, this metric tells us what proportion of this allowable isused by our solutions.
Strategy 3) rank the top BMPs based on the amount of nitrogen reduction per dollar spent.

## Slide 42: Results:
All three-ranking methodologies:
Table: Top choice BMPs based on the all three-ranking methodology
Identify the similarities and differences between top-ranked BMPs,
2

## Slide 43: Results:
Obtaining the total ranking of each BMP by adding the associated ranking to induvial BMPs.
Provide recommendations to reduce the optimization time
3
Notes: Item 3) Recommend an innovative approach to reduce the optimization time through a new BMP ranking strategy. Each ranking mythology has advantages and disadvantages.we come up with an approach to to use a weighted average to come up with a common approach that get benefits of all three rankings.results are presented here.

## Slide 44: Results:
Similarities:
Top BMP choice: Nutrient management lawn or farm
The pasturelands: Off-stream watering facilities
Differences:
More diversity in BMP types was in agricultural settings compared to urban ones.
Identify the similarities and differences between top-ranked BMPs,
2

## Slide 45
1
Pareto solutions spilt for rural and urban counties
2
Frequency of BMPs extracted
3
7 out of 200 BMPs are frequently used in Pareto solutions
“Innovization” Study on CBW Problem Variable Reduction
4
Re-optimize using only 7 BMPs

## Slide 46: Reoptimization Using Innovization Results on Berkeley County
Notes: Comment: Gregorio please replace this figure with the all combined counties
GT: I have the plot.
Comment2: Gregorio: Please add a new figure for Berkely here. I modified the one from your papr that which include other methods (e.g., preferred)
GT: I understood that you want a figure comparing the result of only one strategy vs the Control one. Here I have the accumulated PF, using Strategy 2 (which was the selected one for Hoda’s paper).
GT: I also added the next slide (which is hidden) with the attainment surface.

## Slide 47: Reoptimization Using Innovization Results on Berkeley, Hardy, Jefferson, and Mineral Counties (Combined)
Notes: Comment: Gregorio please replace this figure with the all combined counties
GT: I have the plot.
Comment2: Gregorio: Please add a new figure for Berkely here. I modified the one from your papr that which include other methods (e.g., preferred)
GT: I understood that you want a figure comparing the result of only one strategy vs the Control one. Here I have the accumulated PF, using Strategy 2 (which was the selected one for Hoda’s paper).
GT: I also added the next slide (which is hidden) with the attainment surface.

## Slide 48: Results:
Recommend the selection of the top seven BMPs from the overall column for optimization.
Hypothesis: this approach could significantly reduce the optimization processing time while producing more cost-effective BMP implementation plans.
Can be used in developing the initial population in other counties within the state of West Virginia.
Provide recommendations to reduce the optimization time
3
Notes: we recommend the selection of the top seven BMPs from the overall column for optimization.
This group of BMPs can be used in developing the initial population for the optimization process in other counties within the state of West Virginia.
Hypothesis: this approach could significantly reduce the optimization processing time while producing more cost-effective BMP implementation plans.

## Slide 49: Reoptimization Using Innovization Results on Berkeley County
Notes: Comment: Gregorio please replace this figure with the all combined counties
GT: I have the plot.
Comment2: Gregorio: Please add a new figure for Berkely here. I modified the one from your papr that which include other methods (e.g., preferred)
GT: I understood that you want a figure comparing the result of only one strategy vs the Control one. Here I have the accumulated PF, using Strategy 2 (which was the selected one for Hoda’s paper).
GT: I also added the next slide (which is hidden) with the attainment surface.

## Slide 50: Prototype Interactive Web Tool
Input-output through the web portal (Done)
1
Collects scenario for optimization (Done)
2
NSGA-III is invoked and calls CAST for evaluation (Done)
3
Calls Decision-making Dashboard for analysis of Pareto solutions (Remaining)
4
Re-optimize using "Innovized" principles until satisfied (Partially Done)
5

## Slide 52: Decision-Making Methods
Deb, K., Sundar, J., Reddy, Uday, B., and Chaudhuri, S. (2006). Reference point based multi-objective optimization using evolutionary algorithms. International Journal of Computational Intelligence Research (IJCIR), 2(6), 273–286.
Decision-making:
A systematic approach to pick a preferred solution
  A-posteriori Trade-off analysis
  A-priori Aspiration based approach
  Interactive EMO-MCDM
    DM provides preference information during optimization

## Slide 53: Remaining Tasks
Multi-criterion Decision-making (MCDM) to choose a single solution
Dashboard for interactive applications
  A partial framework is completed
Converted Oxygen optimization to combine multiple loadings
Completion of all BMP types: Land conversion, Animal, Manure transport, etc.
More than two-objective optimization
Demonstration through workshops and tutorials
Scale-up study to multi-state and watershed level optimization
Harnessing hardware parallelism

## Slide 54
Computational Optimization and Innovation
Thank you